## Slide 1: Request for Increasing Wood Densities in the Asotin Creek IMW: 19-1499 Stephen Bennett1,2, 3, Nick Bouwes1,2, 3, and Joe Wheaton1,3 Utah State University1, Eco Logical Research Inc. 2 , and Anabranch Solutions, LLC3.
Notes: Hello
Thanks for this opportunity to apply for restoration funding for the Asotin IMW
The IMW is different than the typical Salmon Recovery project –
The State and Federal agencies tasked with Salmon Recovery are relying in IMWs to assess the effectiveness of a variety of restoration approaches
Asotin IMW is assessing LWD effectiveness in wadeable streams (small to medium sized streams) that make up about 90% of a typical watershed

## Slide 2: Outline
Where are we
Why the request
Where are we going
IMW end goal
Proposal
Increase wood density
Promote overbank flow
Notes: Outline and Message
1. Why are were requesting more restoration funds?
2. What is the request for?
3. What is the end goal and why should you care?

## Slide 3: Where are we?
Design
South Fork
(197)
Trial
Pit Tag Arrays
North Fork
(135)
Charley
(208)
Increase Wood Density
PRE-TREATMENT
POST-TREATMENT
Monitoring
South Fork
(116)
2008
2010
2009
2011
2015
2013
2012
2019-2021?
2017
2018
2016
2014
Notes: Here’s where we are
Completed design and pre-treatment monitoring
Completed Restoration treatments ~ 9 miles and 650 structures
Now we just need to monitor response of habitat and fish for ~ 10 years (minimum recommended by RCO review of IMWs)

## Slide 4: Where are we?
Bouwes et al. 2011 – CHaMP protocol
Camp and Wheaton 2014 – Field data collection apps
Conner et al. 2014 – Survival juvenile steelhead
Camp 2015 – High density large wood effectiveness in Asotin
Bennett et al. 2016 - IMW progress and lessons learned
Bouwes et al. 2016 – Implementing adaptive management
Wall et al. 2016 – Net rate of energy intake (NREI) model
Wall et al. 2017 – Changes in NREI after restoration
Wathen et al. 2017 – Assessment of mark-recapture assumptions
Loughin et al. 2018 – Staircase design experiments (resubmitting)
Wheaton et al. 2019 – Low-tech restoration manual
Notes: A list of publications directed related to Asotin IMW
Highlighted key ones related to this presentation in BOLD
Not just working on specific IMW goals – developing and testing approaches to improve our ability to ASSESS wood treatments

## Slide 5: Where are we?
Cost/year average ~ $260,000
Cost/mile ~ $60,000
Total IMW to 2021 - $4,667,000
Notes: Breakdown of Monitoring and Restoration costs by COMPLETED and PROPOSED
Take away – we will have completed 14 years of monitoring (including all the infrastructure)
and ~ 9 miles of restoration for the cost of some 1 mile restoration projects ...
You can’t get better value for $$$ for an IMW … some restoration projects cost this much a MILE

## Slide 6: Why the request?
Notes: Why are we requesting restoration funds - it was all in our restoration and adaptive management plans
Here is our adaptive management plan for treatment sections (complexes of many structures)
I will zoom into the red box

## Slide 7: Why the request?
Notes: If structures are not functioning or some have moved ... What to do?
Assess whether NATURAL wood recruitment is taking place of added wood (we are seeing wood recruitment – but not enough)
Therefore – we should add more wood

## Slide 8: Proposal
Steelhead MSA, priority restoration
Increase density of large wood
Promote overbank flow
Notes: Summary of Asotin IMW wood increase proposal

## Slide 9
Restoration Effectiveness
Notes: Pan out and things look really good – we went here for the Nov RTT (South Fork Asotin)

## Slide 10
Notes: But several places look like this or “worse”
We predicted this in 2012 … and we had a AM plan to deal with changes

## Slide 11
Condition of structures 5 years (South Fork), 4 years (Charley), and 3 years (North Fork) after construction (n = 580).
Structure Integrity Wood Movement & Capture
Notes: This graph shows results from 5 years of surveys of 580 structures (first 3 years of treatments);
as you can see 10-15% of structures completely moved, however,
almost the same number of new structures were created

## Slide 12: Proposal - Increase wood density
Notes: Proposal is to add wood via tree falling

## Slide 13: Proposal - Increase wood density
Notes: And grip hoisting

## Slide 14: Proposal – Increase wood density
BDAs
PALS
Notes: And build some PALS and BDAs in key areas

## Slide 15
North Fork Asotin Creek – Maintenance
Notes: Want to promote more of this and trap more sediment to raise the bed

## Slide 16
Notes: Like this – this is not is a fish survey site which limits our ability to detect changes in habitat and fish

## Slide 17
Notes: However, keep in MIND
Charley and South Fork flow at ~ 5 cfs in summer ….
Overbank flow likely limited to main channel during LOW FLOW when only WOOD is added

## Slide 18
Terrace
Upland
Valley bottom
Beavers can connect floodplain at low flows …
Notes: NEED BEAVERS TO CREATE floodplain connection during low flow
There is evidence that by installing large volumes of LWD we can help beavers re-colonize areas that they have been extirpated from – the wood essentially improves streams conditions and provides both food and cover for beavers
As well as dissipating flows that helps dams to persist

## Slide 19: End goal
Fish response?
Why?
Geomorphic Units
Total Migrants
Female escapement
Year
Notes: Can wood additions SIGNIFICANTLY increase fish production?
Why – what are the mechanisms?

## Slide 20: End goal
Climate change buffer
(USEPA 2006)
West Region
240,000 km wadeable
130,000 km degraded
Notes: But BIG Picture
This IMW will be used to inform WADEABLE stream restoration throughout WEST – scope of degradation is high
AND these streams are where the WATER comes FROM
Potential to BUFFER climate change impacts are huge … there will be less snow in mountains
We need to slow water/runoff down …

## Slide 21: Acknowledgements
Funding
NOAA, Pacific Coastal Salmon Recovery Fund
NOAA, Pacific States Marine Fisheries Commission
Salmon Recovery Funding Board
Bonneville Power Administration
Collaboration and Support
Snake River Salmon Recovery Board
Integrated Status and Effectiveness Monitoring Program
US Forest Service
Washington Department of Fish and Wildlife
Utah State University
Asotin County Conservation District
Notes: First – I have many acknowledgements to make
Much of research is conducted in southeast Washington where I work in the Columbia River Basin studying ESA salmon and steelhead populations and recovery strategies
The principle funding agency is NOAA’s Pacific States Marine Fisheries Commission and Washington States Salmon Recovery Funding Board
Many other local groups in se Washington